## Slide 1: LECTURE 7: Peripherals PIT TIMER
EMBEDDED SYSTEM COURSE

## Slide 2: Learning Goals
Understanding basis concepts about timer, specifically in KL46 SoC.
Understanding on how to configure the PIT module in KL46.
Understanding on how to configure the Real Time Clock – RTC.
Notes: Overview on KL46 Timer modules
Periodic Interrupt Timer (PIT) Module
Real Time Clock (RTC) Module

## Slide 3: Table of contents
Overview on KL46 Timer modules
Periodic Interrupt Timer (PIT) Module
Real Time Clock (RTC) Module

## Slide 4: Table of contents
Overview on KL46 Timer modules
Periodic Interrupt Timer (PIT) Module
Real Time Clock (RTC) Module

## Slide 5: Overview on KL46 Timer modules
The KL46 supports following timer modules:
  Timer/PWM Module (PWM): two to eight channel timer which supports input capture, output compare, and the generation of PWM signals to control electric motor and power management applications. The counter, compare and capture registers are clocked by an asynchronous clock that can remain enabled in low power modes.
  Periodic Interrupt Timer (PIT)
  Low power timer (LPTMR): can be configured to operate as a time counter with optional prescaler, or as a pulse counter with optional glitch filter, across all power modes, including the low-leakage modes. It can also continue operating through most system reset events, allowing it to be used as a time of day counter.
  Real Time Clock (RTC)
This lecture only focuses on PIT, the remaining modules are advance topics and target on student’s self-study. Refer link.

## Slide 6: Table of contents
Overview on KL46 Timer modules
Periodic Interrupt Timer (PIT) Module
Real Time Clock (RTC) Module

## Slide 7: Periodic Interrupt Timer (PIT)
PIT is an counter that generates an output signal when it reaches a programmed count. The output signal is often used to trigger an interrupt
PIT may be one-shot or periodic.
  One-shot timers will signal only once and then stop counting.
  Periodic timers signal every time they reach a specific value and then restart, thus producing a signal at periodic intervals. Periodic timers are typically used to invoke activities that must be performed at regular intervals

## Slide 8: Periodic Interrupt Timer (PIT) – cont.
Typical applications:
  To implement a clock
  To check user input periodically
  To monitor environment changes
  To switch between programs
  Count how many cycles/times the MCU has been elapsed since last restart.

## Slide 9: Periodic Interrupt Timer (PIT) – cont.
Simple explanation:
  A timer is basically a counter of clock cycles.

## Slide 10: Periodic Interrupt Timer (PIT) – cont.
Time Period
  = (count + 1) × clock cycle time = (count + 1) / clock frequency
EX: The clock frequency is 50MHz.
The needed time period is 5.1ms.
What is the count value?
Notes: 256000

## Slide 11: Periodic Interrupt Timer (PIT) – cont.
How to program a timer?
  Set up count value
  Check if the timer expires
  Configure interrupt, if interrupt is to be used
  Read current value (if supported)
Notes: 49999

## Slide 12: Periodic Interrupt Timer (PIT) – cont.
KL46 PIT Module
  The KL46 PIT module is an array of two timers that can be used to raise interrupts and trigger DMA channels.
  As its name: “Periodic timers” the KL46 PIT timer is automatically restart when counter reaching to zero
  The KL46 PIT block diagram

## Slide 13: Periodic Interrupt Timer (PIT) – cont.
The KL46 PIT register descriptions

## Slide 14: Periodic Interrupt Timer (PIT) – cont.
The KL46 PIT register descriptions
  PIT Module Control Register (PIT_MCR) : enable/disable the PIT timer clock and control the timer when PIT enters debug mode
  PIT Upper/Lower Lifetime Timer Register (PIT_LTMR64H PIT_LTMR64L): counting the MCU lifetime (number of cycle has been elapsed from last restart)
  Timer Load Value Register (PIT_LDVALn): set timeout counter number
  Current Timer Value Register (PIT_CVALn): indicate the current timer position
  Timer Control Register (PIT_TCTRLn): configure the specific timer enable/disable, setup the chain mode, timer interrupt enable
  Timer Flag Register (PIT_TFLG): holds that status of the timer interrupt flag.

## Slide 15: Periodic Interrupt Timer (PIT) – cont.
Some scenarios on setting the timer counter
  The counter period can be restarted, by first disabling, and then enabling the timer with TCTRLn[TEN].

## Slide 16: Periodic Interrupt Timer (PIT) – cont.
Some scenarios on setting the timer counter
  The counter period of a running timer can be modified, by first disabling the timer, setting a new load value, and then enabling the timer again

## Slide 17: Periodic Interrupt Timer (PIT) – cont.
Some scenarios on setting the timer counter
  It is also possible to change the counter period without restarting the timer by writing LDVAL with the new load value. This value will then be loaded after the next trigger event

## Slide 18: Periodic Interrupt Timer (PIT) – cont.
Some scenarios on setting the timer counter
  If we want to setup a timer with timeout period > maximum timer counter:
  Expect timeout > 232/fPIT
  In this case we can consider to use the chain timer (timer2 counter will be started to count when timer1 counter reached to zero)

## Slide 19: Periodic Interrupt Timer (PIT) – cont.
Some examples
  The PIT clock has a frequency of 50 MHz.
  Timer 1 creates an interrupt every 5.12 ms.
  Timer 2 creates an interrupt every 30 ms.
// turn on PIT
PIT_MCR = 0x00;
// Timer 1
PIT_LDVAL1 = 0x0003E7FF; // setup timer 1 for 256000 cycles
PIT_TCTRL1 = TIE; // enable Timer 1 interrupts
PIT_TCTRL1 |= TEN; // start Timer 1
// Timer 2
PIT_LDVAL2 = 0x0016E35F; // setup timer 2 for 1500000 cycles
PIT_TCTRL2 |= TEN; // start Timer 2

## Slide 20: Periodic Interrupt Timer (PIT) – cont.
Some examples
  The PIT clock has a frequency of 100 MHz.
  Two timer module are available
  An interrupt shall be raised every 1 hour.
// turn on PIT
PIT_MCR = 0x00;
// Timer 1
PIT_LDVAL1 = 0x23C345FF;0x00000009; // setup timer 1 for 600 000 000 cycles
PIT_TCTRL1 = TIE; // enable Timer 1 interrupts
PIT_TCTRL1 |= TEN; // start Timer 1
// Timer 2
PIT_LDVAL3 = 0x00000009;; // setup timer 2 for 10 cycles
PIT_TCTRL2 = TIE; // enable Timer 2 interrupt
PIT_TCTRL2 |= CHN; // chain Timer 2 to Timer 1
PIT_TCTRL2 |= TEN; // start Timer 2

## Slide 21: Table of contents
Overview on KL46 Timer modules
Periodic Interrupt Timer (PIT) Module
Real Time Clock (RTC) Module

## Slide 22: Real Time Clock – RTC
In modern device today, almost has clock which can be display in LCD with time and date information.
The Real Time Clock – RTC is used to maintain and control the date & time which runs off its own battery.
The RTC also used to other functions including alarm and event scheduling.

## Slide 23: Real Time Clock – RTC (con.t)
KL46 RTC Module
  The RTC module features include:
    32-bit seconds counter with roll-over protection and 32-bit alarm
    16-bit prescaler with compensation that can correct errors between 0.12 ppm and 3906 ppm
    Register write protection: Lock register requires POR or software reset to enable write access
    1 Hz square wave output
    The RTC remains functional in all low power modes and can generate an interrupt to exit any low power mode.

## Slide 24: Real Time Clock – RTC (con.t)
KL46 RTC Module
  Internal connection
RTC
SIM
NVIC
MCG
RTC OSC
Timer clock
Register access
clock
interrupt

## Slide 25: Real Time Clock – RTC (con.t)
KL46 RTC Module
  Registers:
    All registers must be accessed using 32-bit writes and all register accesses incur three wait states.
    Write accesses to any register by non-supervisor mode software, when the supervisor access bit in the control register is clear, will terminate with a bus error.

## Slide 26: Real Time Clock – RTC (con.t)
KL46 RTC Module – Step to configure the RTC
In system powered-up state
  Configure the SIM for access to the RTC register block
  /*enable the clock to SRTC module register space*/
  SIM_SCGC6 = SIM_SCGC6_RTC_MASK;
After VBAT POR or software reset
  Enable the oscillator
  RTC_CR |= RTC_CR_OSCE_MASK;
  The time invalid flag is set and must be cleared by writing the seconds register to a valid value
  RTC_TSR = 0x00000005;
  Enable the counter
  RTC_SR |= RTC_SR_TCE_MASK;

## Slide 27: Real Time Clock – RTC (con.t)
KL46 RTC Module – Step to configure the RTC
Using time compensation use the RTC_TCR register
  Select compensation interval value (1 to 256)
  Select time compensation register value (-127 to +128)
  RTC_TCR = 0x0000_0100; //apply every 2 seconds
  RTC_TCR |= 0x0000_0080; // add 128 cycles to the prescaler register
To lock the Status, Control, or Time Compensation Registers use the RTC Lock register (hard lock).
  Can only be cleared on Vbat POR or software reset via RTC_CR
  RTC_LR = 0x00000010; // lock SR, CR, and TCR. Will require VBAT POR

## Slide 28: Summary
Understanding about the basic concepts regarding periodic timer and especially the KL46 PIT and RTC timer modules.
Understanding on how to setup a simple timer and a chain timer.
Understanding on how to setup a Real Time Clock

## Slide 29: Question & Answer
Thanks for your attention !

## Slide 30: Copyright
This course including Lecture Presentations, Quiz, Mock Project, Syllabus, Assignments, Answers are copyright by FPT Software Corporation.
This course also uses some information from external sources and non-confidential training document from Freescale, those materials comply with the original source licenses.