## Slide 1: LECTURE 8: Peripherals UART
EMBEDDED SYSTEM COURSE

## Slide 2: Learning Goals
Understanding basis concepts about UART and how to transmit/receive data via UART connection.
Introduce about RS232 protocol.
Understanding on how to configure the KL46 UART module.
Notes: Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 3: Table of contents
Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 4: Table of contents
Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 5: Introduction to UART
UART: Universal Asynchronous Receiver/Transmitter
A UART maybe used when:
  High speed is not required
  An inexpensive communication link between two devices is required
UART communication is very cheap:
  Single wire for each direction (plus ground wire)
  Asynchronous because no clock signal is transmit.
  Relatively simple hardware.
Very widely used

## Slide 6: Table of contents
Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 7
UART applications
PC to Device
PC to PC
PC to Internet

## Slide 8
UART applications
Become much less common
Largely been replaced by faster, more sophisticated interfaces
  PCs: USB(peripherals), Internet(Network)
  Chip to chip: I2C, SPI
Still use today when simple low speed communication is needed: for debugger.

## Slide 9: UART functions
Transmitter
  Convert from parallel to serial
  Add Start and Stop bits
  Add parity bit
Receiver
  Convert from serial to parallel
  Remove Start and Stop bits
  Check and remove parity bit

## Slide 10: Table of contents
Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 11: Data transmission
Use a single wire for transmission
Each bit has fixed time duration determined by the transmission rate.
  Example: a 1200 bps (bit per second) UART will have a 1/1200 s or about 833.3 us bit duration.

## Slide 12: Data transmission
The Start bit marks the beginning of a new transmission.
When detected, the receiver synchronizes with the new data stream.

## Slide 13: Data transmission
Next follow the data bits (7 or 8).
The least significant bit is sent first.

## Slide 14: Data transmission
The parity bit is added to make the number of 1’s even (even parity) or odd (odd parity).
This is can be used by the receiver to check for transmission errors.
Use of parity bit is optional.

## Slide 15: Data transmission
The Stop bit marks the end of transmission.
Receiver checks to make sure it is “1”.
Separates one word from the start bit of the next word.

## Slide 16: Data transmission
In the configuration shown, it takes 10 bits to send 7bits of data.
Transmission efficiency is 70%.

## Slide 17: Data transmission
An example of sending the ASCII letter “W”- 1010111.

## Slide 18: Table of contents
Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 19: Data Reception

## Slide 20: Data Reception

## Slide 21: Data Reception

## Slide 22: Data Reception
Receiver also verifies that stop bit is “1”, if not, reports “framing error” to host system.
New start bit can appear immediately after Stop bit.
Receive will resynchronize for each Start bit.

## Slide 23: UART options
UARTs usually have programmable options:
  Data: 7 or 8 bits.
  Parity: even, odd, none, mark, space.
  Stop bits: 1, 1.5, 2.
  Baud rate: 300, 1200, 2400, 4800, 9600 , 19.2k, 38.4k, 57.6k. 115.2k…

## Slide 24: UART Data throughput
Data throughput Example
  Assume 19200 baud, 8 data bits, no parity, 1 stop bit
    19200 baud19.2kbps
    1 start bit + 8 data bits + 1 stop bit = 10 bits  It takes 10 bits to send 8 bits of data.
    19.2 kbps * 8/10 = 15.36 kbps.
    How many KB (kilobytes) per second:
    =15.36 * 1KB / 8192 bits = 1.875 KB/s

## Slide 25: Table of contents
Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 26: RS232
RS232 is the most common UART standard.
  Used by PC serial ports.
  RS232 does not use positive logic.
  Logic 1 is any signal from -25V to -3V
  Logic 0 is any signal from +3V to 25V
  The range -3V to 3V is a transition region that is not assigned to a logic level.
  RS232 connecting between a DTE (Data Terminal Equipment) and a DCE (Data Circuit-terminating Equipment).

## Slide 27: RS232 signals
Hardware flow control = RTS/CTS handshaking

## Slide 28: Table of contents
Introduction to UART
UART Applications
Data Transmission
Data Reception
RS232
Freedom KL46 UART

## Slide 29: Freedom KL46 UART Block Diagram

## Slide 30: Freedom KL46 UART Block Diagram

## Slide 31: Features
Full-duplex operation
13 bit baud rate selection.
Programmable 8-bit, 9-bit or 10-bit data format.
Double-buffered transmitter and receiver with separate enables
Independent FIFO structure for transmit and receive.
DMA interface.
Three operation mode: Wait, Stop and Debug mode.

## Slide 32: UART signals

## Slide 33: Baud Rate Registers
UARTx_BDH
  SBR[4-0]: 5 higher bits of the 13 bits UART baud rate bits
UARTx_BDL
  SBR[7-0]: 8 lower bits of the 13 bits UART baud rate bits
  Where BRFD = the BRFA[4:0] field divided by 32

## Slide 34: Control Registers
UARTx_C1:
  M: 9-bit or 8-bit select mode
  PE: Parity Enable
  PT: Parity Type (Even, Odd)
  UARTx_C2:
  TIE: Transmit Interrupt or DMA Transfer Enable
  TCIE: Transmission Complete Interrupt Enable
  RIE: Receiver Full Interrupt or DMA Transfer Enable
  TE: Transmitter Enable
  RE: Receiver Enable

## Slide 35: Status Register
UARTx_S1
  TDRE: Transmit Data Register Empty Flag
  TC: Transmit Complete Flag.
  RDRF: Receiver Data Register Full Flag.
  FE: Framing Error Flag.
  PF: Parity Error Flag.
UARTx_S2
  MSBF: Most Significant Bit First.
  RAF: Receiver Active Flag.

## Slide 36: Data Register
UARTx_D
  RxTx[7:0] :
    Reads return the contents of the read-only receive data register.
    Writes go to the write-only transmit data register.

## Slide 37: Example UART Init
Enable the clock for the port associated with the UART pins you want to use (SIM_SCGCx)
Enable UART pins (PORTx_PCRn)
Enable the UART module clock (SIM_SCGCn)
Configure the UART control registers for the desired data format
  Number of data bits (UARTn_C1[M] and UARTn_C4[M10])
  Parity and parity type (UARTn_C1[PE,PT])
  MSB or LSB first (UARTn_S2[MSBF])
  Data polarity (UARTn_S2[RXINV] and UARTn_C3[TXINV])
Configure the baud rate (UARTn_BDH and UARTn_BDL)
Enable the receiver and/or transmitter (UARTn_C2[RE, TE])

## Slide 38: Reference
http://www.powershow.com/view/af8e1-ZTk2Z/20_UART_flash_ppt_presentation
http://en.wikipedia.org/wiki/Universal_asynchronous_receiver/transmitter
KL46 Reference Manual

## Slide 39: Summary
Understanding about the basic concepts regarding UART such as its applications, how the data has been transmitted as well as received.
Understanding about RS232 standard.
Understand on how to configure the Freedom KL46 UART module.

## Slide 40: Question & Answer
Thanks for your attention !

## Slide 41: Copyright
This course including Lecture Presentations, Quiz, Mock Project, Syllabus, Assignments, Answers are copyright by FPT Software Corporation.
This course also uses some information from external sources and non-confidential training document from Freescale, those materials comply with the original source licenses.